## Slide 1: uELM Configuration
uELM:
  Dedicated component configuration within CIME
  Data Atmosphere / Coupler / BGC-active ELM
KiloCraft:
  data toolkit for kmELM
Partition schemes
  Round-robin partition
IO configuration
  SCROPIO
    PnetCDF and ADIOS
Performance profiling/archiving
  GPTL and PACE website
Dedicated E3SM component setting for uELM Simulation
Notes: Here is our solution featuring a dedicated E3SM component configuration within the CIME framework, as illustrated in the figure. The solution integrates a data atmosphere model that reads large atmospheric forcings from disk, conducts temporal interpolation, and sends the data to the Coupler. The Coupler then performs grid mapping if necessary and forwards data to uELM. uELM, in turn, retrieves large input data from disk, executes massive parallel computations, and generates substantial data, such as history data and restart files, at user-defined time intervals. To facilitate this process, we've developed a data toolkit called kiloCraft to format and prepare several necessary uELM input data, including domain, atmospheric forcings, and surface properties data. Currently, uELM supports six partition schemes, as illustrated in the top figure. In our study, round-robin partition is selected for our scaling experiments. The I/O configuration of uELM depends on fine-tuning the Software for Caching Output and Reads for Parallel I/O (SCORPIO), a high-level I/O Library containing APIs for two parallel I/O libraries, PnetCDF and ADOIS. Performance profiling is conducted using built-in general-purpose timing libraries (GPTL), and we have published and archived our performance data on a public website hosted and managed by Oak Ridge National Laboratory.

## Slide 2: Input and output data streams
Major Input files:
Atmospheric Forcing
Aerosol
CO2 Profile
Domain File
Surface Properties
Initial Condition (empty if the simulation use cold start)
Plant Functional Types (PFT) Parameters
Nitrogen Deposition
Phosphorus Deposition’
Population Density
Lighting Location, Frequency and Possibility
Output files:
History: ~500 Variables (float, int)
Restart: 390 Variables (double)